## Slide 1
Computational architecture
Physical inputs
Spot electricity prices
PV generation
Reference demand
Battery limits, losses
and operating costs
Hourly preferences
α = 0.20 / 0.25 / 0.30
ωt: time slots intraday template
Under Strategies A and B, α enters the rule determining how much photovoltaic electricity is self-consumed directly
Energy flows allocation and post-dispatch valuation.
Strategy A : fixed-threshold rules
Direct PV rule; PV charging.
Discharge to household load.
Strategy B: adaptive price rules
Direct PV rule; price look-ahead.
Grid charging; battery export.
Strategy: C rolling optimization
Hourly re-solved 24 h schedule.
price-oriented objective.
Schedule of the operating decisions are independent of α and ωt
Energy trajectory
PV use; charge / discharge
Grid imports and exports
Continuous SOC
Feasibility checks
Energy flows allocation snapshots
Post-dispatch valuation
Analytical P2P price rule
All exports as injection proxy
Consumption and buyer utilities
Reported SW and surplus indicators
Utility-indifference price benchmark
Reporting and secondary analysis
Hourly results → daily / monthly / annual summaries
Coefficient α comparisons; active-sample price medians; descriptive Fourier profiles
Fourier analysis is post-processing, not part of the dispatch controller.

## Slide 2
Dispatch strategies. Implementation-aligned pseudocode
A fixed-threshold rules
01
Calculate direct PV use from α, hourly ω, price, PV and demand.
02
Apply usable-energy self-discharge; carry SOC across days.
03
Set daily price thresholds at 1/3 and 2/3 of the min–max range.
04
At a low price, charge eligible PV surplus within battery power limits.
05
At a high price, discharge to residual household demand within reserve limits.
06
Give discharge priority if candidates overlap; update SOC and store flows.
B adaptive 24 h rules
01
Use the same direct-PV rule and continuous SOC accounting as A.
02
Read up to 24 supplied future prices; set 0.30 / 0.70 range thresholds.
03
Assess whether charging for later self-consumption or sale is worthwhile over the next 24 hours. Allow discharge only above a predefined reserve of 10% of battery capacity, increased to 30% during Hours 17–22 to retain a larger evening reserve.
04
With PV surplus, charge PV when low-price OR arbitrage criteria hold.
05
Without PV surplus, charge from grid only when low-price AND arbitrage criteria hold.
06
At a high price, serve load first, then export; prevent simultaneous charge/discharge.
C hourly rolling optimisation
01
Fix direct PV use at min(load, PV); start with the current SOC.
02
Form a window of min(24, remaining hours) using supplied price/PV/load data.
03
Minimise electricity purchasing and battery wear costs, accounting for assumed export revenues and predefined incentives for PV storage and reduced grid imports during high-price hours.
04
Include constraints of energy balance, SOC continuity and battery power limits, applying their respective reserve rules, as in strategies A and B. additionally require 90% SOC at the end of each planning window (only as a pre-determined model choice for C, not as an optimum level derived by any solver).
05
First solve using Linear Programming (LP). If the solution schedules simultaneous charging and discharging, use Mixed-Integer Programming (MIP) with binary switches to prevent both within the same hour.
06
Αpply only the current hour’s decision, update stored energy, and repeat the 24-hour optimization hourly. Reuse each capacity’s annual schedule across α values, recalculating utility and welfare for each case.
COMMON FINAL STEP Calculate utility, P2P prices and reported welfare after the operating trajectory is known.

## Slide 3
Illustration: architecture and pseudocode
Inputs
Simulation engine
(8,760 hours)
Outputs
Electricity prices
(pₜ)
PV generation
(Gₜ)
Household demand
(Dₜ)
Battery parameters
(Emax, ηch/dis, degr.)
Utility function
U(Cₜ)
P2P market settings
(α, λ, matching)
Demand response
(utility-based)
Battery dispatch
(Strategy A / B / C)
Grid interaction
P2P trading
(blockchain market)
Welfare calculation
SOCₜ
Energy flows
(PV, battery, grid, P2P)
Self-consumption
P2P volumes and prices
Prosumer utility
and surplus
Grid dependence
Welfare decomposition
Strategy A – Rule-based
1. If Gₜ > Dₜ: charge battery (up to Emax)
2. Else if priceₜ > threshold and SOCₜ > SOCmin: discharge
3. Else: keep SOCₜ
4. Update SOCₜ and apply degradation
Strategy B – Forecast-based
1. Obtain forecasts: Ĝₜ₊₁:ₜ₊₂₄, D̂ₜ₊₁:ₜ₊₂₄, p̂ₜ₊₁:ₜ₊₂₄
2. Compute charge/discharge thresholds
3. If expected high price and SOCₜ > SOCmin: discharge
4. If expected surplus PV: charge
5. Update SOCₜ and apply degradation
Strategy C – 24h rolling optimisation
1. Solve 24h optimisation problem (t … t+23):
max Σ U(Cₜ) − cost_grid + revenue_P2P − degradation
subject to battery, power balance and market constraints
2. Implement first-hour decision
3. Roll to next hour and repeat